Basic Spectrum Analyser Settings

---
Guess the Wave form

---
Guess the Wave form
Freq = 100 Hz
Amplitude = 0.7 V
VRMS	= 0.495 V

---
Guess the Wave form
Freq = 120 Hz
Amplitude = 1 V
VRMS	= 0.7071 V

---
Guess the Wave form
Freq = 150 Hz
Amplitude = 1.3 V
VRMS	= 0.495 V

---
Guess the Wave form
Freq = 190 Hz
Amplitude = 1.8 V
VRMS	= 1.273 V

---
Sum of the all 4 wave

---
Sum of Sine waves
FFT Plot
Sine waves

---
Fast Fourier Transform Plot

---
Fast Fourier Transform Plot in Voltage Scale

---
Spectrum analyser
- A spectrum analyzer is used to measure and analyze the frequency spectrum of RF (Radio Frequency) signals.
- It helps visualize signal amplitude versus frequency, making it essential for RF design, EMI/EMC testing, and debugging wireless communications.

---
Block Diagram

---
General Alternative Names
- Frequency Analyzer
- RF Spectrum Analyzer
- Signal Analyzer
- Spectral Analyzer

---
Basic Settings
- Set the Frequency Range
- Adjust Amplitude Settings
- Triggering & Sweep Settings

---
Frequency Range
- Methods to Set Frequency Range
  - Using Center Frequency & Span
  - Using Start and Stop Frequencies

---
Center Frequency & Span
- Center Frequency: Set it to the signal’s expected frequency.
- Span: Define how wide the spectrum should be around the center frequency.

---
Using Start and Stop Frequencies
- Start Frequency: The lowest frequency you want to observe (HIGH PASS FILTER).
- Stop Frequency: The highest frequency you want to observe (LOW PASS FILTER).

---
Adjust Amplitude Settings
- Reference Level: Set to avoid signal clipping or low visibility.
- Attenuation: Adjust input attenuation to prevent overload.
- Resolution Bandwidth (RBW): Defines frequency resolution (lower RBW = better detail but slower scanning).
- Video Bandwidth (VBW): Smooths the display (should be ≤ RBW).

---
Resolution Bandwidth

---
Video Bandwidth

---
Zero Span

---
REFERENCE
- Youtube (R&S): https://www.youtube.com/watch?v=P5gxNGckjLc
- Simulation (LT Splice): https://github.com/KAMALESH-EEE/FFT
- Web: https://www.keysight.com/blogs/en/tech/rfmw/2020/05/28/spectrum-analysis-basics-part-2-whats-in-a-spectrum-analyzer

---
Thank You